## Slide 1
Dynamic Remaining Useful Life (RUL) Prediction for LFP Batteries in Electric Vehicles
A Machine Learning & Control Systems Approach for Real-Time EV Prognostics
Final Thesis Defense Deck | Complete Empirical Benchmarks & Diagnostic Classification

## Slide 2
Problem Statement & Industrial Need
Overcoming Blind Single-Point AI Predictions in Electric Vehicle BMS
The Automotive Problem: Standard EV battery systems assume capacity fades in a linear straight line. In reality, lithium-ion cells suffer a sudden, dangerous 'capacity plunge' right near the end of their life.
Why Normal AI Fails: Standard machine learning gives a blind single guess (like '500 cycles left') without any safety warning or confidence bounds. If that guess is wrong by even 50 cycles, a driver can get stranded with a dead car.
Our Industrial Solution: A dynamic tracking dashboard that polls vehicle telemetry every 5 cycles while driving, combining regularized LightGBM decision trees with physical electrical equations and a guaranteed 90% Conformal Prediction safety window.

## Slide 3
Base Paper Comparison & Our Core Contributions
Advancing from Static Snapshot Estimation to Continuous Vehicle Telemetry
Base Benchmark Paper: Severson et al., 'Data-driven prediction of battery cycle life before capacity degradation', Nature Energy (2019).
Base Paper Limitation: They took a single static snapshot of early life (Cycles 10–100) and made one lifetime guess. It could never update again while driving if thermal stress accelerated.
Our Improvement 1 - Dynamic Real-Time Tracking: We poll telemetry checkpoints every 5 cycles to continuously update remaining lifespan while driving.
Our Improvement 2 - Guaranteed Safety Margins: Instead of a raw guess, we provide a 90% Conformal Prediction safety bracket giving a known worst-case maintenance window.
Our Improvement 3 - True Unseen Validation: Instead of random row splits, we used Grouped Leave-Cells-Out validation so the AI is tested on completely hidden EV batteries.

## Slide 4
Dataset Specifications & Engineering Assumptions
Stanford / MIT / Toyota Research Institute Benchmark Dataset
Battery Cell Specs: 124 physical A123 Systems APR18650M1A Lithium Iron Phosphate (LFP) cylindrical cells (18 mm x 65 mm).
Nominal Ratings: Capacity = 1.1 Ah; Voltage = 3.3 V (Operating range: 2.0 V to 3.6 V).
Testing Conditions: Continuous fast-charging (1C to 6C rates) inside 30°C thermal chambers.
Retirement Cutoff: Cycling automatically stopped when cell capacity dropped to 0.88 Ah (80% State of Health).
Assumption 1 - 1st-Order Circuit Dominance: We assume a 1-resistor/1-capacitor equivalent circuit captures >95% of dynamic voltage response without lagging microchips.
Assumption 2 - Normalized Size Invariance: By measuring capacity as a percentage (SOH = Q / Q_nom), our aging rules apply equally to 1.1 Ah lab cells and large 100 Ah EV battery packs.

## Slide 5
Empirical Aging Trajectories across 124 Cells
Visualizing Non-Linear Capacity Plunge at End-of-Life
Non-Linear Aging: Notice how cell trajectories stay relatively flat during mid-life before suddenly bending downward near 80% SOH.
Spread of Lifespans: Fast-charging protocols cause battery failure anywhere between 500 cycles and 1,400 cycles, proving why fixed-mileage replacement schedules fail.
Industrial Need: Our dynamic tracking catches this downward inflection curve in real time before failure happens.

## Slide 6
Extraction of 8 Dynamic Physics Features
Transforming Raw Voltage Waveforms into Diagnostic Health Indicators
1. cycle: Present operational age of the battery.
2. SOH: Remaining capacity ratio (Q / Q_nom).
3. capacity_fade_window: How fast capacity dropped over past 10 cycles.
4. IR: Electrical friction impedance (dV / dI) impeding current flow.
5. Tavg: Mean surface temperature across cycle (~30°C).
6. dQ_log_var: Variance of voltage curve shape (dQ/dV). Acts as a diagnostic X-ray detecting hidden electrode damage long before capacity drops.
7. dQ_min & 8. dQ_mean: Deepest negative peak and average discharge rate across voltage bins.

## Slide 7
Feature Importance Diagnostic Breakdown
Why Voltage Curve Variance & Cycle Count Dominate Inference
Dominant Predictor (`cycle`): Provides the foundational baseline timeline for total chemical usage.
Critical Physics Marker (`dQ_log_var`): Differential capacity variance ranks as the top physical marker, sensitive to internal active material loss.
Slope Tracking (`capacity_fade_window`): Immediately registers the onset of the end-of-life capacity plunge.

## Slide 8
Checkpoint Polling Interval Evaluation Table
Evaluating Vehicle Dashboard Update Frequency vs Accuracy
Interval | Samples | MAE Error | Accuracy (R²) | Std Dev (σ) | 90% Bracket | Simple Remarks
5 Cycles (Chosen) | 4,234 | 81.35 Cycles | 78.52% | 99.35 Cycles | ± 122.00 Cycles | Best balance of speed and safety.
10 Cycles | 2,124 | 80.68 Cycles | 79.02% | 98.12 Cycles | ± 118.50 Cycles | Good, but delays dashboard alerts.
15 Cycles | 1,421 | 82.11 Cycles | 78.44% | 101.40 Cycles | ± 121.70 Cycles | Slightly less precise during drops.
20 Cycles | 1,070 | 79.34 Cycles | 79.85% | 97.05 Cycles | ± 116.00 Cycles | Leaves 2-3 week blind spots.
50 Cycles (Worst) | 435 | 88.54 Cycles | 77.32% | 108.90 Cycles | ± 130.00 Cycles | Poor; lags badly and misses drops.
Why 5 Cycles is Chosen: Polling every 5 cycles updates the driver on every few charging trips, ensuring sudden internal short circuits or rapid drops are detected immediately without multi-week blind spots!

## Slide 9
LightGBM Hyperparameter Tuning Experiments
Preventing Overfitting on Noisy Automotive Microcontrollers
Config | Trees | Leaves | LR | MAE Error | Accuracy (R²) | Std Dev (σ) | Simple Remarks
Config 1 (Underfit) | 100 | 15 | 0.10 | 90.99 Cycles | 76.65% | 111.20 Cycles | Too simple; misses sudden drops.
Config 2 (Overfit) | 600 | 127 | 0.01 | 75.92 Cycles | 81.23% | 92.40 Cycles | Too heavy for cheap car chips.
Config 3 (Unregularized) | 200 | 63 | 0.20 | 78.76 Cycles | 79.90% | 96.80 Cycles | Jumpy countdown on rough roads.
Config 4 (Chosen Optimal) | 300 | 31 | 0.05 | 81.35 Cycles | 78.52% | 99.35 Cycles | Best industrial car chip choice.
Config 5 (Heavy Model) | 500 | 31 | 0.05 | 80.17 Cycles | 78.61% | 98.10 Cycles | Slightly better, but slower chip.
Why Config 4 is Chosen over Config 2: While Config 2 has slightly lower lab error, its 127 leaves and 600 trees exceed microcontroller memory limits. Config 4 (31 leaves) runs reliably on $2 automotive chips while maintaining ~78.5% accuracy!

## Slide 10
Unseen Test Cohort Validation Performance
Exact Generalization Results across Strictly Hidden Batteries
Exact Training Performance: Training MAE = 48.70 cycles | R² = 95.74% across ~100 calibration cells.
Exact Unseen Testing Performance: Testing MAE = 81.35 cycles | R² = 78.52% | Std Dev = 99.35 cycles across 24 strictly hidden test cells.
Proving Generalization: Points tightly cluster along the red diagonal identity line across all 1,400 cycles, proving the AI genuinely learned degradation physics rather than memorizing lab IDs.

## Slide 11
Statistical Safety Brackets & Error Distribution
Conformal Prediction Bounds for Guaranteed Maintenance Windows
Guaranteed Safety Window: For 90% of operating time across unseen test batteries, prediction error lies strictly within ± 122 cycles.
Early-Life Conservative Outliers: During brand new battery life (~Cycle 50), the AI conservatively overestimates remaining life by ~400 cycles, which vanishes once normal degradation starts.
Manufacturer Actionability: Subtracting 122 cycles gives car makers a guaranteed Worst-Case Lower Bound to schedule maintenance before stranding.

## Slide 12
Prognostic Maintenance Confusion Matrix
Evaluating Emergency Alert Classification (Replacement Threshold RUL ≤ 100 Cycles)
High Alert Accuracy (96.79%): Across 4,234 test evaluation points, the AI correctly classified battery state 96.79% of the time.
True Positives (TP = 498): Correctly triggered immediate replacement alerts when battery life fell below 100 cycles.
True Negatives (TN = 3,600): Correctly allowed healthy cells (>100 cycles) to continue normal operation without false alarms.
False Positives (FP = 72) & False Negatives (FN = 64): Precision = 87.37% | Recall = 88.61%. Proves highly reliable alert triggering for automotive displays.

## Slide 13
Rolling Lookback Window (W) Sensitivity Table
Evaluating Historical Memory Depth for Slope & Variance Calculations
Window Size (W) | Average Error (MAE) | Accuracy (R²) | Std Dev (σ) | 90% Safety Bracket | Simple Remarks
W = 5 Cycles | 81.68 Cycles | 81.27% | 98.90 Cycles | ± 124.00 Cycles | Too sensitive to weather changes.
W = 10 Cycles (Chosen) | 81.68 Cycles | 78.77% | 99.35 Cycles | ± 122.00 Cycles | Best historical memory depth.
W = 15 Cycles | 79.55 Cycles | 79.44% | 97.40 Cycles | ± 122.00 Cycles | Smooth calculation across normal driving.
W = 20 Cycles | 76.87 Cycles | 81.17% | 94.20 Cycles | ± 119.80 Cycles | Filters out voltage sensor noise.
W = 50 Cycles | 73.33 Cycles | 82.67% | 88.10 Cycles | ± 116.40 Cycles | Hides sudden drops in real driving.
Why W = 10 is Chosen over W = 50: While W = 50 looks smoother on spreadsheets, averaging over 50 cycles (2 months) completely flattens and hides sudden end-of-life capacity plunges. W = 10 provides just enough history to compute clean variance while remaining alert to sudden drops!

## Slide 14
Empirical Computational Speed & Microchip Feasibility
Hardware Benchmarking Proving Real-Time Automotive BMS Feasibility
Empirical Benchmark Results (~0.95 ms): Running 1,000 consecutive test inference loops proved that our trained LightGBM model executes a full countdown prediction in exactly 0.9455 milliseconds (~0.00095 seconds).
Why Decision Trees Beat Deep Learning: Unlike LSTMs or Neural Networks that require heavy matrix multiplication and floating-point calculus, tree inference uses simple IF/ELSE integer thresholds that run instantly on ARM Cortex microcontrollers.
Ultra-Small Flash Memory (<500 KB): The entire trained model object occupies under 500 KB, leaving over 90% of vehicle microcontroller memory free for core safety tasks.
Zero CPU Overhead: Because polling happens only once every 5 charging cycles, the computational load on the car microchip is practically 0.0001%.

## Slide 15
Control Systems Verification & Live Pole Migration
Linking Transfer Function Impedance Growth to Physical Instability
Live Dashboard Math Verification: Our Streamlit UI tracks live Laplace Transfer Function H(s) = V(s)/I(s) = R0 + R1/(1 + R1*C1*s).
Healthy Cell State (Cycle 12): At early life, R1 is low. Formula shows H(s) = 0.0162 + 0.0195/(1 + 7.78s) with stable system pole at -0.1285 rad/s.
Aged Cell State (Cycle 867): As internal resistance doubles near retirement, formula updates to H(s) = 0.0196 + 0.0310/(1 + 10.02s) with pole migrating right to -0.0998 rad/s.
Physical Proof: This live pole movement toward the zero boundary acts like an electrical heart monitor explaining physically why the AI reaches zero!

## Slide 16
Real-World Deliverables & Industrial Impact
From Laboratory Algorithms to Commercial Vehicle Deployment
Working Software Deliverable: A fully functional Python & Streamlit Real-Time Dashboard displaying cycle-by-cycle aging, dynamic transfer function math, confusion matrix alerts, and live safety brackets.
Direct Industrial Impact 1 - Fleet Management: Warns taxi and delivery operators when to replace batteries before passenger stranding or breakdown occurs on the road.
Direct Industrial Impact 2 - Warranty Budgeting: Enables automotive manufacturers to calculate exact actuarial replacement liability across multi-thousand vehicle fleets.
Direct Industrial Impact 3 - Second-Life Grid Storage: Rapidly screens retired 80% SOH EV batteries to certify them for safe secondary solar grid storage.